## Slide 1: Industrial Computer Vision Detection, Identification and Tracking of Lego Bricks
Group 1 - Pascal Hövel (101625), Korbinian Hörmann (105766)
Final presentation 21.06.2021

## Slide 2: Overview
Camera calibration (intrinsic)
Detection (Preprocessing, Segmentation (Color based, HSV), Postprocessing,
Artificial environment (reproducable bounding conditions)
Classification of Lego Pieces
  Multiclass Object Classification in images using CNN
    Data generation
    Training the model (GPU -> Google Colabs)
    Deploy the model on a RaspberryPi (TensorflowLite, Transfer model format)
Multi-object tracking in videos (based on distance & features)
Final demo on video (live)
Possible improvements

## Slide 3: Camera Calibration
16 images used for intrinsic calibration
Intrinsic parameter used to undistort the image
Intrinsic parameter are saved to .json file
.json file is read on the raspberry pi

## Slide 4: Preprocessing, Segmentation, Postprocessing
Short Revision (with example-images out of deliverable 3):
Preprocessing: Undistortion, Shrink Resolution, Bilteral-Filter and Median-Filter
Segmentation: Colorbased HSV-Thresholding
Postprocessing: Morphological Opening
Raw (undistorted)
After bilateral
After bilateral and median
HSV Thresholding ….

## Slide 5: Artificial Environment
Light Source: Multiple brightness-levels
3 different light modes (cold to warm)
Raspberry Pi
Bucket
Camera
Camera-Arm
Lego Bricks
Underground
Light-Source: Led-ring

## Slide 6: Multiclass Object Classification on images
Using Convolutional Neural Networks (CNNs)

## Slide 7: Supervised Machine Learning
Goal: find patterns in input data and map this input data to a certain class
Prerequesite: enough labeled data in order to approximate to learn a good mapping from input data to a certain class
Labled data
Training and prediction

## Slide 8: Convolutional Neural Networks - Overview
CNNs are neural networks which contain layers that extract features automatically from raw image data (latent structures not seen/difficult to be designed by humans)
Those features can then be used to solve ML tasks (e.g. classification)
Prerequisites:
needs large amounts of labelled training data
needs massive computational resources (e.g. GPUs)

## Slide 9: Convolutional Neural Networks - Example
reduce input size
Preserving most important information
Convolution (Kernels)
Pooling
e.g. to find edges

## Slide 10: Data Generation
Goal: Build a labeled dataset of Lego pieces, on which the object classification model can be trained
Demo: image_acquisition.py

## Slide 11
Data Generation
Final dataset: ~ 1100 images (224, 224, RGB encoded) of 5 different classes

## Slide 12
The data is split into training, validation and test data (80, 10, 10)
The ditribution of the different labels is fairly even in each sub data set
Split the data

## Slide 13: Training the model on GPU (Google Colab)
Convert dataset to grayscale images
  Reduces input
  Focus on shapes, not colors
Perform data augmentation
  Artificially increases the size of data and the variance of data samples
  Random flip
  Random contrast
  Random rotation
Train the model
  Epochs: 6
  Batch size: 32
  Loss: sparse_categorical_crossentropy
  Optimizer: Adam
Evaluate the model
  Accuracy on test data: ~ 93%

## Slide 14: Example predictions

## Slide 15: Deployment on RaspberryPi
Use of TensorFlow Lite: open source deep learning framework for on-device inference
Pipeline
Open TODO

## Slide 16: Multi object tracking in videos
Distance based approach:
detected_pieces = {}
for each new frame
  segment image -> detect Lego pieces
  for each detected Lego piece:
  if position not in already in detected pieces + threshold
  generated UID, predict class & extract other features
  add new piece to detected_pieces
  else
  update position of already existing Lego
Pseudo code

## Slide 17: Live demo – video stream
The script lego_brick_detection.py detects Lego pieces in the video stream and uses a tflite model which was trained on Google Colab to predict the class of the lego pieces.
Each piece gets it’s unique id and is tracked over time.

## Slide 18: Live demo – final overview
After hitting 'ESC', two windows are shown.
Overview: contains information about all the detected pieces, the second one only shows the Id, extracted image, predicted class of this piece.
Possibility to save image: in case this predicted id is correct, those columns can be clicked and the images are saved to the 'dataset/' folder in order to increase the size of the dataset with which the model can be trained.

## Slide 19: Possible improvements
Prediction model
Build smaller model
Quantize the .tflite model
Try out different architecture
(e.g. YOLO)
Data
Add more training data of pieces where the prediction model makes mistakes
Improve image quality
Object Tracking
Implement a more complicated solution for object tracking

## Slide 20: Questions?